PROJECT    PROFILE

ON

FIBRE FOAM FOR SEAT CUSION AND BEDDINGS

July 2013

PREPARED BY

K’S TECHNICAL AND MANAGEMENT CONSULTANTS, VADODARA,

www.technicaltex.com PH: +919825244940

FOR

OFFICE OF TEXTILE COMMISSIONER, MINISTRY OF TEXTILES

INDEX

CHAPTER									PAGE

PRODUCT AND ITS APPLICATIONS					2

AN OVERVIEW OF MARKET						3

SUGGESTED PROJECT SIZE						4

RAW MATERIALS:

AVAILABILITY, REQUIREMENT AND COST			5

TECHNOLOGY ASPECT							6

MANPOWERAND UTILITY: REQUIREMENT			7

INFRASTRUCTURE RQUIREMENT					8

PROJECT COST AND MEANS OF FINANCE				9

FINANCIAL PROJECTIONS						10

CRITICAL FACTORS / KEY ELEMENTS				11

RAW MATEIAL, PLANT AND MACHINERY SUPPLIERS		12

CHAPTER   I

Product   and its Applications

Fiber foams are a substitute for the conventional PU foams.  These are produced using Hollow cross section Polyester fibers bound together with low melt fibers or bonding chemicals.   The Performance of Fiber based foam is acceptable for many end uses.  The technology of making foams using fibers has been perfected in the last few years and many high end applications have already started using these fiber foams in place of conventional Polyurethane foams). Fiber Foams are produced using a Pollution free Thermo bonding Process.

The Fiber foams have distinct advantage of a Non-Toxic process unlike conventional foams which use high poisonous chemicals like MDI or TDI (Toulene Di Isocyante). Formation of foam like structure using Polyester fibers is achieved through melting the surface of a small percentage of fibers or with adhesive spray and bonding them simultaneously. Fiber foams can be made Flame Retardant by using the right type of Polyester Fiber.

The bonding is done by binder fibers or adhesives, the quantity and type of fiber can engineer the properties required in the end use. Fiber foams can be produced from as low as 30 gms per sq m and upto 3000 gms per sq m.  Generally for most applications, a low melt Polyester fiber or Polypropylene fibers are used in the range of 5 to 10% depending on the properties desired in the final products.

The typical end uses for fiber foams can be categorized into two types:

- Technical Uses

- Sound Absorption device in Auditoriums

- Noise Attenuator in Automotives

- Sound Insulation in Domestic Appliances

- Air filter in Desert coolers and Air Conditioners

- Commodity Uses

- Foam Substitute in furniture and Bedding

- Covering of PU foam for better comort

- Filling inside Quilting

- Thermal insulation pads for light weight washable carry bags

- Water resistant purse linings etc.,

- Washable wadding in winter wear

- Distribution layer in Hygiene( Diaper and Sanitary napkins)

An important criteria is that these are recyclable whereas the competing chemical foam product is non-recyclable.

CHAPTER II

An Overview of the Market

The Global market for Nonwovens is estimated to be about 7 million tons and nearly 12% of this market (840,000 tons) is estimated to be manufactured using thermobond technology.

The applications of fiber foam for technical uses is at infancy in India, as most of the existing manufacturers are having equipment that is suitable for making only low density and  light weight products.  It is the capability to produce high density and high weight product that will increase the user base for this product.

Currently the production in India for wadding is estimated to be around 35,000 tons per year. This is produced mainly on second hand and localized equipments and are capable of producing nonwovens upto 600 gms per sq m.

They are generally used in Quilting used on the surface of Foam beddings. Due to export of Garments from India and overall increase in manufacture of ready made garments the market projected is nearly 80,000 tons in the coming years.

The market size will increase when better uniformity products and high density foam is produced.  The technical end uses of this market in acoustics, thermal insulation and seating foams is itself expected to generate a demand of 50000 tons in the coming years for these applications only.

The fabric is generally produced in a minimum width of 1.5 mtr.

Currently there are about 25 wadding manufacturers in India spread all over the country who are producing low density material in the weight range 50 to 500 gsm.  These are made on second hand conventional machines which are capable of producing low density product only and are sophisticated enough to make High density foams  upto 3000 gms per sq m that is envisaged in this project  for Upholstery, Bedding, Automotive, Thermal insulation,  Noise control end uses.   The significant players in the market in India are

- Gokuldas Exports, Bangalore- Makes wadding for Garments and quilts

- Suvi Exports- Delhi  Makes Waddings for Quilts

- JP nonwovens- Mumbai- Makes waddings for quilts and Garment industry

- Jhanji Textiles (P) Ltd., Delhi-  Makes a wide range for quilts and insulation

- Venus Interlinings Private Limited, Jaipur-  Makes  wide range for quilts

- Star Comfort Industries, Bengaluru

- Khushee International, Rajkot-  Polyester and Cotton  based waddings

- Times Fiberfill, Kolkata-  Waddings for Quilts and Beddings industry

- Klin Products, Morbi-  Wadding for Mattress and insulation

CHAPTER   III

Suggested Project Size and Location

Currently the products are produced in India on low capacity lines.  These have technical limitations in terms of density of product, uniformity and range of product to be produced in one line.

A 3 mtr wide line with capability to produce products in the weight range 60 to 3000 gms per sq m is proposed in this project report.  The estimated capacity for this project is about 1500 tons per annum maximum, depending on the product being produced.

The machinery has to be imported from China, Korea or Europe and configured to make a wide range of products for the Indian market.

CHAPTER IV

Raw Materials

- 3D x 44 mm length-  Polyester Hollow fiber

- 6D x 51 mm length- Polyester Hollow Fiber

- 9D x 60 mm length- Polyester Hollow Fiber

- 6D x 44 mm length- Low melt Polyester fiber

- 6D x 44 mm length- Teijin Elastomeric fiber

- 6D x 44 mm length- PP fiber

CHAPTER   V

Technology Aspect

The choice of Nonwovens machinery and Raw materials used are important for the achieving the final product performance.

The Manufacturing Process of Fibre Foam has following steps

- Fiber Opening

- Fiber Blending

- Carding

- Laying

- Thermo bonding in Ovens

- Winding or Sheet cutting

The bonding of fibers is done by the low melt fibers.  To get a good quality material it is essential that these 5 to 10% bonding fibers be blended homogeneously with the Polyester hollow fibers. To achieve this effectively, mixing bins are used in blending. A thorough blending also gives a uniform product.  Carding using air lay cards are found to be more effective particularly for the higher weight products.

High capacity thermo bonding ovens with proper heat transfer design is essential for achieve a product uniformity and good output. Using Direct Gas burning is the most cost effective way of providing energy for the production line.

When high quality thermo bonding is not demanded by the end use, it is quite common to use Poly Propylene fiber as binding fibers.

To get a highly resilient foam, special fibers are available from companies like Teijin. These improve the elastic recovery of foam produced and also give more comfortable feel to the product.

CHAPTER     VI

Manpower and Utility for 3 shift working

Manpower

Plant Manager			1

Shift Supervisors		4

Operators			35 ( including helpers 15 nos.)

Technicians			4

Marketing Manager		1

Accts/Admin			3

Sales				5

CEO				1

Total			          54

Utilities

Installed Power Opening and carding			150Kw

Thermal Bonding oven drives				30Kw

Gas or fuel for oven burner				8 cu mtr/hr or 80KW heating

Thermo bonding oven

Compressed air                                                       	5NM3 /min

CHAPTER VII

Infrastructure   Requirements

Land						1200 SQ M

Plant Building Requirements   		40 mtr length x 10 mtr width x 5 mtr height

Utilities, compressor and other area               10 m x 5 mtr

Raw Material storage and Finished goods

storage-  					10 m x 10 m

Office	Building				10 m x 7 m

Effluent:   					NIL

CHAPTER    VIII

Project Cost and Means of Finance

| PARTICULARS | Rs. Lakhs |
| --- | --- |
| Land 1200 sq m x 900 per sq m | 11 |
| Building 620 sq m x 6750/sq m | 42 |
| Plant and Machinery- imported Korea $1.9 Million x Rs.60/$ | 1140 |
| Lighting, air conditioning etc | 25 |
| Margin for Working Capital | 125 |
| Total | 1343 |

Means of Finance

| PARTICULARS | Rs. Lakhs |
| --- | --- |
| Capital | 403 |
| Term Loan | 940 |
| Total | 1343 |

CHAPTER     IX

FINANCIAL PROJECTIONS

| PARTICULARS | FIRST YEAR |
| --- | --- |
| PRODUCTION AT 60% CAP Utilisation ( 100% capacity 4000 Kg /day)-330 days | 792 TPA |
| PRODUCT- Average | 300 gms per sq m |
| SALES PRICE PER Kg | Rs. 170 |
| RAW MATERIAL Polyester fiber 75/kg+ low melt 200/kg -5% | Rs. 95 |
| CONVERSION COST | Rs. 35 per Kg |
| OPERATING MARGIN PER Kg | Rs. 40 per Kg |
| OPERATING PROFIT per anum | Rs. 316 lakhs |
| Payback Period Estimated | 3 years |

CHAPTER X

Critical Factors   /  Key Elements

- Availability of thermal energy at competitive rates is essential for the project to be competitive.

- Skilled operators are required  for reducing operating wastages

- Consumers for the product within short distance from the factory. This will reduce transportation cost for the bulky material like fibre foam.

- Closeness to industry segment for which major production is sold. Typically like Filtration, Auto seats or furniture or bedding or noise control etc.

CHAPTER XI

Machine Suppliers

| S. No. | Name of Supplier | Country of Origin |
| --- | --- | --- |
|  | Trutzschler | Germany |
|  | Santex | Switzerland |
|  | Jiangsu Jingcheng | China |
|  | Shyngwei | China |
|  | Boo Kwang Tech | Korea |
|  | Yin Yang | China |
|  | CTMC | China |

CHAPTER XII

Raw Material Suppliers

Polyester Fiber

| S. No. | Name of Supplier | Country of Origin |
| --- | --- | --- |
|  | Reliance Industries Ltd | Mumbai |
|  | Indo Rama Industries | New Delhi |
|  | Futura Organics | Chennai |
|  | Teijin Fibers | Japan |
|  | Advansa | Turkey |
|  | Chang Lang | China |
|  | Dafa chemicals | China |

Polypropylene Fiber

Zenith Fibers			Baroda

Radici				Italy

Asota				Austria

Domo fibers			Belgium